## Slide 1: Internet of Things Using Node-Red and Alexa
AnOJA rajalakshmi
School of engineering

## Slide 2: What is IoT?
Internet of Things (IoT) means learning and interacting with millions of things including services, sensors, actuators, and many other objects on the Internet.
IoT allows objects to be sensed and controlled remotely across networks.
Notes: Things are wide variety of devices like Wifi connected or has access to internet

## Slide 3: IoT Classification
Image Courtesy: Yuichi Kawamoto, Hiroki Nishiyama, Nei Kato, Naoko Yoshimura, and Shinichi Yamamoto, "Internet of Things (IoT): Present State and Future Prospects", IEICE Transactions on Information and Systems, vol. E97-D, no. 10, pp. 2568-2575, Oct. 2014

## Slide 4: Evolution of Human Machine Interaction
1. Screen and Keyboard, Text-bases UI computers.
Notes: Through monitors, people can read the outputs from computers.
The input is captured by keyboards, which is the only way.
And the “Computers” act in the middle to carry out calculation or simply do the tasks given

## Slide 5: 2. Mouse, GUI computers
Notes: A computer mouse is a pointing device (hand control) that detects two-dimensional motion relative to a surface. This motion is typically translated into the motion of a pointer on a display, which allows a smooth control of the graphical user interface.

## Slide 6: 3. Touch Screen, Portable devices.
Notes: A touchscreen is an input and output device normally layered on the top of an electronic visual display of an information processing system. A user can give input or control the information processing system through simple or multi-touch gestures by touching the screen with a special stylus and/or one or more fingers

## Slide 7: 4. Voice-control
Notes: Voice control on smart phones: Siri, Cortana
Google home: Hands-free help from the Google Assistant
Amazon Voice service called Alexa inside Echo, Echo Dot,

## Slide 8: Applications of Voice Control and IoT
Control of Home devices
Outdoor
Security
Weather Monitoring
Navigation
Industrial automation
Notes: We can create customized skills or voice commands which can be used in day today basic

## Slide 9: Lets get into the project
Hardware:
  MCUs: Raspberry Pi, Intel Edison, ESP8266, ESP32
  Sensors: Photo Light Sensor, DHT11(Temp/Humidity), PIR, Door Sensor, Seed groove kit
  Actuators: Servo Motor, LED, Relays, Buzzer
  Hands free speaker: Amazon Echo
  Web Services:
  Alexa Skill Kit
  Amazon Web Services(AWS)
  IBM Bluemix
  Twilio
  Third party services: Open weather, Google account for email, Mosquitto
  Protocols:
  MQTT
  HTTP
  SSH

## Slide 10: Raspberry Pi 3 Model B
BCM43438 wireless LAN and Bluetooth Low Energy (BLE) on board
Quad Core 1.2GHz Broadcom BCM2837 64bit CPU
Features: GPIO, UART, I2C and SPI
1GB RAM
40-pin extended GPIO
4 USB 2 ports
Runs Linux and Node RED

## Slide 11: Intel Edison
Processor: 22 nm Intel® SoC that includes a dual-core, dual-threaded Intel® Atom™ CPU at 500 MHz and a 32-bitIntel® Quark™ microcontroller at 100 MHz
RAM: 1 GB
Wireless: Dual-band (2.4 and 5 GHz) IEEE 802.11a/b/g/n
40 general purpose GPIO features:
  SD card: 1 interface
  UART: 2 controllers
  I2C: 2 controllers
  SPI: 1 controller with 2 chip selects
  I2S: 1 controller
  GPIO: Additional 14 (with 4 capable of PWM)

## Slide 12: ESP8266
Low-cost microcontroller including full TCP/IP stack
Produced by Shanghai-based Chinese manufacturer, Espressif Systems.
CPU: 32-bit RISC Tensilica Xtensa L106 @ 80 MHz.
RAM: 64 kB for instructions; 96 kB of data.
WiFi: – IEEE 802.11 b/g/n – WEP or WPA/WPA2 authentication, or open networks.
Features: 16 GPIO pins, SPI, I2C, UART, 10-bit ADC.
Slide Courtesy: https://github.com/apuder/iot-workshop/blob/master/doc/iot-workshop-slides.pdf

## Slide 13: ESP32
CPU: 240 MHz dual core Tensilica LX6 microcontroller with 600 DMIPS
Integrated 520 KB SRAM
Robust Design: industrial environments with an operating temperature ranging from -40°C to +125°C
2.4 GHz Wi-Fi and Bluetooth combo chip
Ultra-Low Power Management
Features:
  3 x UARTs
  3 x SPI
  2 x I2S
  12 x ADC input channels
  2 x DAC
  2 x I2C
  PWM/timer input/output available on every GPIO pin
Notes: As you see I have listed about 4 different microcontrollers those can be placed anywhere in the world, They need a simple protocol to talk to each other.

## Slide 14: MQTT
Message Queuing Telemetry Transport is a lightweight publish/subscribe protocol with reliable bi-directional message delivery.
Invented in 1999 by Andy Stanford-Clark (IBM) and Arlen Nipper. The original problem was to send sensor data from oil pipelines through a satellite link.
Runs on top of TCP/IP. Both client and broker need a TCP/IP stack.
Event oriented, therefore avoids polling
Notes: This project uses MQTTfx for debugging MQTT messages.
MQTT.fx is a MQTT Client written in Java based on Eclipse Paho.

## Slide 15: Publish / Subscribe
Clients are always connected with a broker.
Both publishers and subscribers are “clients”.
A client sends a message (publisher).
One or more clients receive the message (subscribers).
MQTT uses “topics” to determine which message is routed to which client.
A topic is a “hierarchical structured string”.
Notes: All the red and blue are clients.
The client that publishes is called publisher.
All those receives is called subscribers
Topic is a string word and is hierarchical meaning: home -> living room ->light or home -> living room -> TV will be represented as /home/livingroom/light or home/livingroom/TV

## Slide 16: SENSORS
Notes: DHT11 – Temparature/ humidity sensor
Door Sensor - one reed switch and one magnet, creating a closed circuit. If someone opens an armed door or window, the magnet is pulled away from the switch, which breaks the circuit and triggers an event.
Ultrasonic sensor – Detects the distance between objects
PIR – Passive Infrared Sensor 120 degree
Photo light sensor- resistance decrease when exposed exposed to light

## Slide 17: ACTUATORS
Notes: LEDs are the easiest way to simulate an output

## Slide 18: Example for LED working
Pin D2 is in output mode.
Whenever Microcontroller turns pin D2 high, LED glows.
This process can be controlled from a remote location using different techniques.
LED can be replaced by a Relay which acts like a switch
Notes: The important matter is getting the pin high or low according to our application.

## Slide 19
Pin D4 is in output mode
Relay pins:
  Vcc: connected to 3V3 of NodeMCU
  Gnd: connected to GND of NodeMCU
  Signal: connected to Pin D4
  NO/NC: Normally open/close (Output)
  C: Common (Output)
  Output can be connected to higher voltage up to 250V.
Notes: Reason: Limitation of demo –ing garage door open and other lights

## Slide 20: Alexa
Echo is powered by Alexa
Helps interact with devices in more intuitive way using voice
Developed by Amazon
When you ask Alexa for something, it triggers an Alexa Skills Kit, which is often linked to AWS Lambda to execute the code.
Courtesy: https://www.leverege.com/blogpost/alexa-skills-kit-tutorial

## Slide 21: Basic Examples
Alexa, What is the weather today?
Alexa, trigger find my phone
Alexa, open project demo
Notes: Project Demo: The project aims to control and automate devices using voice. The major advantage of the system is ease of management for the user by not to have his or her phone open and click on certain options to control things or go near the switch to turn it on.